SECTION 098315 - ACOUSTICAL METAL PANELS

GENERAL

SUMMARY

This Section includes the following:

Acoustical metal panels.

SUBMITTALS

Product Data:  For each type of product indicated.

Samples for Initial Selection:  For components with factory-applied finishes.

Size: Minimum 3 inch x 3 inch.

Shop Drawings:  Submit shop drawings showing how panels are to be laid out on walls and ceilings.  Width of panels and location of vertical seams are critical.

QUALITY ASSURANCE

Single-Source Responsibility:  Provide acoustical metal panel units and installation components by a single manufacturer.

Fire Performance Characteristics:  Identify acoustical wall components with appropriate markings of applicable testing and inspecting organization.

Surface Burning Characteristics:  As follows, tested per ASTM E 84.

Flame Spread:  25 or less.

Smoke Developed:  200 or less.

Coordination of Work:  Coordinate acoustical metal panel work with installers of related work including, but not limited to building insulation, gypsum board, light fixtures, mechanical systems, electrical systems, and sprinklers.

DELIVERY, STORAGE, AND HANDLING

Deliver acoustical metal panels to project site in original, unopened packages and store them in a fully enclosed space where they will be protected against damage from moisture, direct sunlight, surface contamination, and other causes.

Handle acoustical metal panels carefully to avoid scratching or damaging units in any way.

PROJECT CONDITIONS

Space Enclosure:

Panels:  All wet work must be complete and dry prior to installation.  Installation shall be carried out where the temperature is between 40 degrees F and 120 degrees F.

PRODUCTS

MANUFACTURERS

Acoustical Metal Panels:

Acoustimetal acoustical metal panels by Acoustical Surfaces, Inc. (Basis of Design)

123 Columbia Court North, Suite 201, Chaska, MN 55318.

952-448-5300, Fax: 952-448-2613.

Toll Free: 1-800-448-3134.

Or equal.

ACOUSTICAL METAL PANELS

Product: Acoustimetal acoustical metal panels.

Description: Perforated metal shell and nonflammable acoustical material.

Shell:

Material: [.040 aluminum] [galvanized steel] [stainless steel].

Perforation: 50% perforation pattern or as selected by Architect.

Finishes: Clear anodized aluminum or optional painted white.

Fill:

Non-flammable, Class A per ASTM E-84, fiberglass free (LEED eligible) Echo Eliminator or Sound Silencer material.

Size: As indicted on Drawings.

Attachment: Mechanical clips.

Applications: Walls, ceilings, steps, machine enclosures for indoor or outdoor.

Sound Absorption Test Data per ASTM C423: Acoustimetal panels with 1" Echo Eliminator fill.

NRC: 0.85.

SAA: 0.87.

EXECUTION

PREPARATION

Measure each area and establish layout of acoustical units to balance border widths at opposite edges of each area.  Coordinate metal panel layout with mechanical and electrical fixtures.

INSTALLATION

Install metal panels per the manufacturer’s written instructions.

CLEANING

Clean exposed surfaces of metal panels.  Comply with manufacturer's written instructions for stripping of temporary protective covering, cleaning, and touchup of minor finish damage.  Remove and replace metal panel components that cannot be successfully cleaned and repaired to permanently eliminate evidence of damage, including dented and deformed metal panels.

END OF SECTION 098315