SECTION 08347 – SOUND CONTROL DOORS

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

SUMMARY

This Section includes sound control doors with STC ratings up to 56.

SUBMITTALS

Product Data: Submit manufacturer's product data and installation instructions.

Test Reports: Upon request submit certified test reports from recognized test laboratories.

Certificates: Submit manufacturer's certificate that products meet or exceed specified requirements.

DELIVERY, STORAGE & HANDLING

Delivery: Deliver material in the manufacturer’s original, unopened, undamaged containers with identification labels intact.

Provide labels indicating brand name, source of procurement, style, size and thickness.

Storage and Protection: Store materials protected from exposure to harmful environmental conditions and at temperature and humidity conditions recommended by the manufacturer.

WARRANTY

Warranty Period:  Two years.

PRODUCTS

MANUFACTURERS

Sound Control Doors:

Studio 3D - Noise S.T.O.P. Soundproof Interior Doors by Acoustical Surfaces Inc. (Basis of Design)

123 Columbia Court North Suite 210.

Chaska, MN  55318.

(800) 448 - 0121.

www.AcousticalSurfaces.com

Or equal.

SOUND CONTROL DOORS

STC ratings: Up to 56 per ASTM E-90.

Door Thickness: 2-3/4" thick, 13 layer composite door assembly.

Pre-hung and Assembly:

Door: [Flush design] [Custom]  [With vision elites] [Single] [Pairs] [As indicated on Drawings].

Frame: [Standard frame] [Custom] [As indicated on Drawings].

Sizes: [Select from standard] [Custom in single or double] [As indicated on Drawings].

Finishes: Stain grade in [Oak] [Maple] [Cherry] [Birch] [Primed Metal] [Any wood species as selected by Architect].

Hardware: Door, frame, trim, handle, hinges, perimeter sound seals and door bottom supplied as part of the tested assembly.

Automatic sill.

Heavy duty hinges (4).

3-point latching system.

Adjustable neoprene mortise jams and seals.

Options: [Dead bolt] [Mortise locks] [Heavy duty closer].

Finishes: [Standard nickel] [Standard brass] [Custom as selected by Architect].

[Optional Vision Lite Kit]: [Metal] [Wood].

Clear glass opening size: [10” x 10”] [6” x 28”] [22” x 28”] [22” x 56”] [Custom].

[Optional Jamb Kit].

Required Installation kit Includes:

2 Packs of Shims.

4 Sets of Heavy Duty Jamb Screws.

Backer Rod.

1 Tube Acoustical Sealant.

EXECUTION

EXAMINATION

Examine openings, substrates, anchorage, and conditions.

Immediately inspect shipment for damage during transit i.e., damage caused by fork lifts, stacking, water stains etc. and disclose to delivery driver prior to signing for receipt.

INSTALLATION

Manufacturer’s Instructions:

Comply with written instructions and of the door manufacturer.

Installation manual is available from manufacturer’s website.

END OF SECTION 08347